# General Issues

The interface definitions in Spice3.Interfaces are identical to Modelica.Electrical.Analog.Interfaces, except for
- Spice3.Interfaces.TwoPort_controlled_sources
- Spice3.Interfaces.VoltageSource
- Spice3.Interfaces.CurrentSource
Why is this the case and does it make sense? Alternatively you could extend the SPICE3 interfaces from the ANALOG interfaces.

Additionally the models
- Spice3.Basic.Ground
- Spice3.Basic.R_Resistor
- Spice3.Basic.C_Capacitor
- Spice3.Basic.L_Inductor
are redundant to the ones in the Modelica.Electrical.Analog library. One solution could be to extend these models from the ANALOG library and apply the required extensions, e.g., the start values.

In the diode model Spice3.Repository.DIODE the voltage drop v between positive and negative pin is not explicitly calculated. I do not know whether the voltage drop v is available in SPICE, but the voltage drop v should certainly be available in Modelica, because it is an important quantity.

The voltage drops of the MOSFET models are also not defined (similar to diode model). For example, the source drain voltage shall be defined since this quantity is often important in a technical analysis.

SPICE3 is formally still dependent on Analog_Development and Spice3_parameterbinding but there is no reference to any class of these libraries. Additionally, incompatible dependencies on the MSL 2.2.1, 3.0 and 3.1 exist. These dependencies, i.e., annotation (uses(...)), have to be removed.
# Units and Parameter Text

In some SPICE3 packages units are not properly declared:
- Spice3.Repository
- Spice3.Repository.Equation
However, physical units need to have a physical representation in Modelica.

Technology parameters have no explanation in the parameter text:
Spice3.Semiconductors.modelcardDIODE
If possible, a grouping of parameters shall be performed in order to more structure the huge amount of parameters.

Some comments contain two question marks at the beginning of the text: "?? ...", e.g., in Spice3.Repository.modelcardMOS; that should be changed

In MODELICA always SI units shall be used. Some quantities are associated with non SI units, e.g. NSS or UO in Spice3.Repository.modelcardMOS. This shall be changed. In case it is intended to build an automatic translation tool from SPICE to MODELICA, the translation from non SI units to SI units has to be taken into account at some point.
# Documentation

In the SPICE3 library the User's Guide is missing as it was specified in the conventions for the MSL.

Throughout the library, the documentation (and this does not include naming conventions of parameters and variables, since the library needs to be written in SPICE style) is not compliant to the documentation guidelines. This does particularly include formatting and structuring rules specified at https://svn.modelica.org/projects/ModelicaDesign/trunk/MSL-Documentation/.

The documentation is often just plain text with arbitrarily used <br> instead of a sound HTML code. Therefore, e.g., the enumerations in Spice3.Sources.V_sin appear as
- it should be set all the parameters definitly...
- normally, there exist ...
instead of
<ul>
     <li>it should be set all the parameters definitly...</li>
     <li>normally, there exist ...</li>
</ul>
# Comments

Should we able to handle
- DC analysis?
- AC analysis?